## Slide 1
SMART WASHROOM
Hygiene Monitoring & Automatic Disinfection System
ESP32 • Dual Occupancy Sensing • Virtual Sensing • Streamlit Dashboard
Project Overview — Revision 2

## Slide 2
The Problem
1
Odor
Poor ventilation and delayed cleaning leave lingering bad odor
2
Blind Spot
No one knows water or disinfectant levels until they run out
3
Manual Inspection
Staff must physically check each washroom repeatedly
4
Expensive Retrofits
Existing smart-toilet systems need full reconstruction
Public washrooms in India
need a low-cost box that
retrofits into an EXISTING
washroom — no rebuilding,
no distributed sensor network.
2

## Slide 3
Proposed Solution
A single retrofit “Smart Hygiene Box” — one ESP32, a handful of sensors, two actuators
SENSORS
LD2410 + IR
MQ135 • HC-SR04
ESP32
Decision
Logic
ACTUATORS
Mist pump
Refill pump
Streamlit Dashboard
Live status now — physical OLED display deferred to Phase 2
Key safety rule: the system NEVER fires the mist pump while either occupancy sensor shows the washroom is in use — corrected during design review.
3

## Slide 4
Hardware at a Glance
E
ESP32
Main controller
L
LD2410 + IR
Dual occupancy sensing
M
MQ135
Air quality / odor
H
HC-SR04
Water tank level
4
4-Ch Relay
CH1 mist · CH2 refill
2
2 × 12V Pumps
Spray + auto-refill (2nd pump was previously idle)
Estimated cost: ≈ ₹2,300–2,600 (both pumps were already owned — lower than the original estimate)
4

## Slide 5
Design Review Caught a Real Safety Gap
BEFORE
Trigger: gas level > 250 ppm,
OR 4 hours since last spray.
Occupancy was never checked —
the mist pump could fire while
someone was still inside.
AFTER
1
Either sensor “occupied” → never spray
2
Occupied → Vacant → baseline spray
3
Still bad air, still vacant → up to 2 extra sprays
4
Cap reached, still bad → stop + flag for manual checkup
5
4h+ idle, vacant → one refresh spray
5

## Slide 6
Virtual Sensing — The Core Contribution
There is no physical level sensor on the disinfectant tank — only the water tank has one (HC-SR04)
Indirect signals
Spray count • timing
Entries • usage history
Trained model
Random Forest /
Gradient Boosting,
vs. a naive counter
baseline
Estimated level
Drives the low-
disinfectant alert —
a real technical
effect, not just
a predicted number
Why it matters: this framing — infer a quantity, then control a real alert/actuator — is what gives the ML work genuine paper and patent value, rather than “a box with sensors in it.”
6

## Slide 7
ML Features — What's Really ML
1
Anomaly Detection
Isolation Forest on air-quality signal
ML
2
Virtual Sensing + Forecast
Regression model estimates disinfectant level & time-to-refill
ML
3
Disinfection Control
Deterministic, occupancy-gated rule — kept safety-critical, NOT a learned model
RULE-BASED
4
Usage Clustering
K-Means across cubicles for traffic patterns
ML
7

## Slide 8
Dataset Validation — Before / After
Metric
Before
After
Longest single spray event
795 min (13+ hrs)
5 min
Sprays while occupied
not checked
0 (verified)
hygiene_score “predictability” (R²)
0.9997 (pure formula)
0.86 (real noise)
Tank ever ran low?
No — stayed 95–100%
Yes — realistic depletion
Cubicles simulated
1
4, distinct traffic patterns
8

## Slide 9
Streamlit Dashboard — 3 Tabs
Live Monitoring
Occupancy, air quality, tank levels, mist status, activity feed
Predictive Maintenance & ML
Disinfectant forecast, anomaly alerts, sensor-agreement panel
Historical Analytics
Peak-hour heatmap, air-quality trends, resource consumption
Primary interface for now — OLED physical display is Phase 2 (an LED gives a simple interim Occupied/Vacant signal)
9

## Slide 10
Current Status & Novelty Angle
Where things stand
• Hardware: partially built
• Data pipeline: validated on synthetic data (4 cubicles)
• Interface: Streamlit live, OLED deferred
• Team: hardware + this ML/DL/DS track + dashboard
Novelty for paper / patent
Not “a box that monitors a washroom” — that already exists (e.g. IPToilet®, patented, deployed in 15 states).
The defensible claim: inferring an unmeasured consumable level from indirect signals, and using that to control a real actuator/alert — not just predicting a number.
India's 2025 CRI guidelines: no working prototype is legally required to file — a sufficiently detailed, enabling description is what matters.
10

## Slide 11
Thank You
Questions & discussion